## Slide 1: VR Knowledge Oculus Mobile Tuning Tech Note
Andy Chen
Prerequisite: Basic OpenGL

## Slide 2: Outline
Basic VR Knowledge
Oculus Mobile Tuning Performance Tech Note

## Slide 3: Virtual Reality Basic Knowledge
Convex Lens
  Distortion Shader Effect
Stereoscopic Rendering

## Slide 4: Convex Lens
Convex Lens Has Lens Distortion Problem
  Need to be solved ? Ans: distortion effect
Convex Lens other problems
  https://en.wikipedia.org/wiki/Optical_aberration
    Distortion
    Chromatic aberration

## Slide 5: Convex Lens Distortion
https://www.youtube.com/watch?v=B7qrgrrHry0

## Slide 6: Barrel Distortion Shader Effect
Two types of shader
  fragment shader
  vertex shader
http://www.geeks3d.com/20140213/glsl-shader-library-fish-eye-and-dome-and-barrel-distortion-post-processing-filters/2/
The distortion effect related with lens

## Slide 7: Stereoscopic Rendering
Simulate human eye because of parallax
  Binocular vision to create depth perception
  Binocular distance (approx 6~6.5cm)
Use two camera as left eye and right eye
  two camera distance called as “Interaxial”

## Slide 8: Interaxial

## Slide 9: Screen Parallax
Convergence Distance

## Slide 10: 3D Glasses

## Slide 11: Convergence (1/2)

## Slide 12: Convergence (2/2)

## Slide 13: General Geometry vs Stereoscopic Geometry
1. Mono camera frustum is symmetric, gluPerpective (FOV and Aspect ratio)
2. Left & right camera frustum is asymmetric, need to calculate and apply to glFrustum
3. For calculation, need get mono camera FOV and aspect ratio
4. calculate top, bottom, left and right plane by using FOV and aspect ratio
5. gluLookAt from left and right camera is different, lookAt center point shift based on mono camera look at center point
mono camera
gluLookAt

## Slide 14: OpenGL Stereoscopic Rendering
Get Left and Right Camera Geometry
  (Get left and right frustum)
  Convergence
  Eye separation
  Aspect ratio
  FOV Y degree
  Near
  Far
Render each camera view to FBO
  get FBO color texture
Prepare plane subdivision mesh
  apply distortion effect with camera texture
  Maybe apply chromatic aberration in fragment shader
Swap buffer for double buffer
or glFlush for single buffer

## Slide 15: Oculus Mobile Tech Note
How Oculus Mobile Tune Performance

## Slide 16: Linux Scheduling
http://man7.org/linux/man-pages/man7/sched.7.html
change thread to SCHED_FIFO
change thread priority
change thread CPU affinity

## Slide 17: VRManager in System Server
reportApplicationInVR( String pkg, boolean activeInVR )
  VR activity should heartbeat to VRManager to check if VR acitivity normal because of VR activity change to FIFO that may cause hang
setThreadSchedFifo( String pkg, int pid, int tid, int prio );
setCPUClockMhz( String pkg, int[] mhz )
setGPUClockMhz( String pkg, int mhz );
releaseCPUMhz( String pkg)
releaseGPUMhz( String pkg)
// CPU mhz: 300,423,653,730,884,960,1037,1191,1268,1498,1575,1728,1959
( 2266,2458 not supported by VrManager)
// GPU mhz: 200,320,389,462,578

## Slide 18: VR Lib listen to Vsync
Each event register broadcast receiver, and then onReceive calls native function to native code
  Headset Plug
  Battery
  Wi-fi
  Phone state
  Volume
Get VRManager proxy to set CPU & GPU clocks

## Slide 19: Tune Performance
Query Object
  Query GPU time
  https://www.opengl.org/wiki/Query_Object
  https://www.khronos.org/registry/gles/extensions/EXT/EXT_disjoint_timer_query.txt
To Make Low Latency
  Front Buffer Rendering (Direct Rendering)
  Time Warp
    https://www.youtube.com/watch?v=WvtEXMlQQtI
  Sensor Head Tracking Prediction
    Related with sensor latency, angular velocity, linear velocity

## Slide 20: Front Buffer Rendering
VRSurfaceManager in system server
  setFrontBuffer
DirectRender.cpp
  Consider tile rendering condition for different GPU platform
  Tile render half screen for each eye
    Force call glScissor half screen
    Half screen as a bin
https://www.khronos.org/registry/egl/sdk/docs/man/html/eglCreateWindowSurface.xhtml
  Create a single buffer

## Slide 21: TimeWarp
Solve the head tracking not sync with rendering
Solve the final head tracking, the image not drawn, and then predict final image based on previous image
TimeWarp is not panacea, it is just approximate image that may cause black edge image because of shifting image
Head Rotation 1
Head Rotation 2
Interpolate head rotation matrix to shift image pixels
Notes: Many people are skeptical on first hearing about this, but for attitude changes, the warped pixels are almost exactly correct. A sharp rotation will leave some pixels black at the edges, but this turns out to be minimally distracting.

## Slide 22: TimeWarp

## Slide 23: TimeWarp
https://www.khronos.org/registry/egl/sdk/docs/man/html/eglCreateContext.xhtml
EGLContext eglCreateContext(EGLDisplay display, EGLConfig config, EGLContext share_context, EGLint const * attrib_list)
IMG_context_priority
  EGL_CONTEXT_PRIORITY_LEVEL_IMG 0x3100
  EGL_CONTEXT_PRIORITY_HIGH_IMG 0x3101
  EGL_CONTEXT_PRIORITY_MEDIUM_IMG 0x3102
  EGL_CONTEXT_PRIORITY_LOW_IMG 0x3103
Share
eglContext
PBuffer Surface
Window
Surface
Warp Thread
High priority to use glContext
VR Thread
RenderToTexture
Draw Surface
There two infinite loop threads
VR thread 2. Warp thread
that dedicate rendering
use this texture to draw to the surface

## Slide 24: TimeWarp
vsync
VR thread
Warp thread
Block until
warp thread render someone eye
Left eye
Right
eye
draw so long
drop fps
previous left eye tex
new right eye tex
Left eye
Right
eye
previous left eye tex
previous right eye tex
Left eye
Right
eye
new left eye tex
new right eye tex
Left eye
Right
eye
new left eye tex
new right eye tex
Left eye
Right
eye
new left eye tex
new right eye tex
thread crash
Left eye
Right
eye
previous left eye tex
previous right eye tex
tex means texture
still can work
generate new texture

## Slide 25: TimeWarp
Each eye image records its texture and transform
That can use timewarp to predict the real image

## Slide 26: TimeWarp

## Slide 27: TimeWarp
TimeWarp.cpp
Predict Head Tracking
return predicted sensor pose
Calculate warp rotation matrix
Calculate the warp rotation matrix given to program

## Slide 28: Head Tracking Prediction
OVR_CAPI.cpp
CAPI_HMDState.cpp
OVR_SensorFusion.cpp

## Slide 29: Distortion Effect related with Lens
OVR_DeviceConstants.h
  Enum DistortionEqnType
Distortion.cpp
OVR_Stereo.h
  Struct LensConfig
OVR_Stereo.cpp
HmdInfo.cpp
  Directly point device lens config

## Slide 30: Others
Chromatic Aberration
  Detail in TimeWarp.cpp shader code
sRGB FrameBuffer
  glEnable( GL_FRAMEBUFFER_SRGB_EXT )

## Slide 31: Performance & Power Consumption Suggestion
Don't use alpha tested / pixel discard transparency
Don't require a lot of cut out geometry
CPU (1191 MHz), GPU (389 MHz)
  If 3D video CPU (884 MHz), GPU(240 MHz)
Don’t use chromatic aberration correction on TimeWarp.
Don’t use 4x MSAA.
Reduce the eye target resolution.
Using 16-bit color and depth buffers may help.
Always make sure textures are compressed and mipmapped.
Apps should always use the multithread
Make low fps such as 30 fps

## Slide 32: Conclusion OpenGL Stereoscopic Rendering with TimeWarp
There are two dedicated render threads (infinite loop)
  VR thread (responsible for generating new eye pose texture )
  Warp thread (high priority thread) (base on VR thread generating eye texture, apply distortion effect and render to window surface)
VR thread (render to texture)
  Get Left and Right Camera Geometry
  Render each eye FBO to texture
Warp thread
  Prepare plane subdivision mesh
    apply distortion effect with camera texture
    Maybe apply chromatic aberration in fragment shader
  Swap buffer for double buffer or glFlush for single buffer

## Slide 33: Reference
http://www.bigeye.url.tw/big5/d_opticstru.htm
http://www.app01.com.tw/paper/254fa6fd-012e-419b-8388-f3853f898ed9
http://rifty-business.blogspot.tw/2013/08/understanding-oculus-rift-distortion.html
https://www.youtube.com/watch?v=B7qrgrrHry0
http://www.uni-koeln.de/~al001/radcor_files/hs100.htm
http://blog.xuite.net/raibura/dorama/51587304-%E6%94%9D%E5%BD%B1+-+%E6%A1%B6,+%E6%9E%95,+%E9%AC%8D+%E7%8B%80+distortion+(%E8%AE%8A%E5%BD%A2)

## Slide 34: Reference
http://www.animesh.me/2011/05/rendering-3d-anaglyph-in-opengl.html
http://www.geeks3d.com/20140213/glsl-shader-library-fish-eye-and-dome-and-barrel-distortion-post-processing-filters/2/
https://www.youtube.com/watch?v=WvtEXMlQQtI
http://on-demand.gputechconf.com/gtc/2015/presentation/S5668-Nathan-Reed.pdf
http://gamedev.stackexchange.com/questions/58408/how-would-you-implement-chromatic-aberration
https://developer.oculus.com/blog/asynchronous-timewarp-examined/